| Position | Capacity | Volume | EP in € | GP in € |
| --- | --- | --- | --- | --- |
| . . . . . . . . | Deliver aluminium supporting flange Limaflex® and install it in accordance with the installation instructions of the manufacturer. Limited flexibility 10 mm thick special profile which can be extended by profile connection elements, with a smooth side and top edge. Profil type: Straight with guide for concrete anchors Art. nr.: P20N25, P20N50 Profile height: 200 mm Length: 2.500 mm (or rather: 5.000 mm) Colour: Aluminium natural colour silver-grey Manufacturer: Sachsenband Metalltechnik GmbH Grothwisch 8 D-25482 Appen, Hamburg Tel. +49 (0) 4101 5179050 Fax +49 (0) 4101 5179051 E-mail: info@sachsenband.de |  |  |
|  |  | . . . . . . . . . . . m | . . . . . . . | . . . . . . . |
| . . . . . . . . | Deliver aluminium shock connectors appropriate for profile type Limaflex® and use them in accordance with the installation instructions of the manufacturer. Article: Shock connectors for optional connection of profile P20N25 in the upper profile area Art. nr.: V20N10 Length: 100 mm Colour: Aluminium natural colour silver-grey Packaging unit: 10 units (VPE) Manufacturer: Sachsenband Metalltechnik GmbH Grothwisch 8 D-25482 Appen, Hamburg Tel. +49 (0) 4101 5179050 Fax +49 (0) 4101 5179051 E-mail: info@sachsenband.de |  |  |
|  |  | . . . . . . . . . . . Units | . . . . . . . | . . . . . . . |

| Position | Capacity | Volume | EP in € | GP in € |
| --- | --- | --- | --- | --- |
| . . . . . . . . | Deliver aluminum concrete anchor with eloxal surface hardening and holding anchor structure - which can also be used as a shock connector (apporpriate for profile type Limaflex®) and use it in accordance with the installation instructions of the manufacturer (inclusion compound). Article: Concrete anchor (shock connector) appropriate for fastening the support ring in concrete (with point or strip base) Art. nr.: BA60 Profile height: 45 mm + 135 mm (mounting depth) Length: 60 mm Colour: Aluminium anodised E6EV1 Manufacturer: Sachsenband Metalltechnik GmbH Grothwisch 8 D-25482 Appen, Hamburg Tel. +49 (0) 4101 5179050 Fax +49 (0) 4101 5179051 E-mail: info@sachsenband.de |  |  |
|  |  | . . . . . . . . . . . Units | . . . . . . . | . . . . . . . |
| . . . . . . . . | Deliver corner element made of aluminum, appropriate for profile type Limaflex® and use it in accordance with the installation instructions of the manufacturer. Article: Corner element (outer and inner 90° corner) for non-positive connection of the profile lengths Art. nr.: EV20N90 Profile height: 200 mm Length: 100 mm + 100 mm Colour: Aluminium natural colour silver-grey Manufacturer: Sachsenband Metalltechnik GmbH Grothwisch 8 D-25482 Appen, Hamburg Tel. +49 (0) 4101 5179050 Fax +49 (0) 4101 5179051 E-mail: info@sachsenband.de |  |  |
|  |  | . . . . . . . . . . . Units | . . . . . . . | . . . . . . . |

| Position | Capacity | Volume | EP in € | GP in € |
| --- | --- | --- | --- | --- |
| . . . . . . . . | Deliver arch element Limaflex® and install it in accordance with the installation instructions of the manufacturer. Limited flexibility 10 mm thick special profile which can be extended by profile connection elements, with a smooth side and top edge. Profile type: arch element, profile segment pre-bent in radii in the factory Art. nr.: P20N Profile height: 200 mm Profile thickness: 10 mm Length: up to 2.000 mm as cut Colour: Aluminium natural colour silver-grey Manufacturer: Sachsenband Metalltechnik GmbH Grothwisch 8 D-25482 Appen, Hamburg Tel. +49 (0) 4101 5179050 Fax +49 (0) 4101 5179051 E-mail: info@sachsenband.de |  |  |
|  |  | . . . . . . . . . . . Units | . . . . . . . | . . . . . . . |